## Slide 1
Camera lens distortions
f = focal length
cx = principal point x coordinate
cy = principal point y coordinate
k1 <1
k1 >1
kn = nth radial distortion coefficient
pn = nth tangential distortion coefficient
skew coefficient between the x and the y axis.

## Slide 2
Camera lens distortions
James & Robson (2014), Mitigating systematic error in topographic models derived from UAV and ground-based image networks, Earth Surface Processes and Landforms
• A trade-off between lens radial distortion term and computed surface form can lead to “doming”

## Slide 3
Camera lens distortions
James & Robson (2014), Mitigating systematic error in topographic models derived from UAV and ground-based image networks, Earth Surface Processes and Landforms
• Doming can be mitigated by incorporating a few oblique camera angles (in red)

## Slide 4
Camera lens distortions
• Doming can be mitigated by incorporating a few oblique camera angles (in red)
• Doming can be mitigated by calibrating the camera parameters by photographing a calibration target
• Doming can be mitigated by georeferencing using ground control points

## Slide 5
Spring 2019 “fly off”—Earth Fissures in Apache Junction, AZ with Alan Deino and David Feary (+others)
DJI Mavic Pro (Deino)
DJI Inspire 2 + ZenMuse camera (Feary)

## Slide 6
Mavic
Inspire + ZenMuse
DEM Comparison: No GCPs, only on board GPS

## Slide 7
Notice the magnitude and sign of the “doming”
Grey surface is the Mavic
Blue surface is the Inspire + ZenMuse